## Slide 1: Downscaling techniques for retrieval of near-surface meteorological fields and turbulence parameters from atmospheric numerical model outputs
Jeremy A. Gibbs
School of Meteorology

## Slide 2: Introduction
The WRF model → self-contained mesoscale modeling system
Flows encompassing global to fine scales

## Slide 3: Introduction
Such capability is appealing to users for whom accurate prediction of turbulence effects is increasingly desirable
Air pollution
  dispersive role of small-scale atmospheric motions
Remote sensing
  accurate description of EM/acoustic wave propagation
BL dynamics, urban effects, and more

## Slide 4: Introduction
How best to adequately represent motions in the range of scales O(≤ 100m) based on numerical model output?
How best to adequately reproduce realistic near-surface flow fields and turbulence parameters?
Several methods based on WRF model applications were evaluated

## Slide 5: Tools
The WRF model (v3.4.1)
University of Oklahoma Large Eddy Simulation (OU-LES) code

## Slide 6: WRF Model Run Options
Mesoscale modeling
  horizontal grid spacing (∆) from 1 km to 4 km
WRF-LES (idealized)
  horizontal grid spacing (∆) from 20 m to 80 m
WRF-LES nested in mesoscale WRF model
  nested domains with ∆ from 12 km down to 40 m
Notes: Ranges

## Slide 7: OU-LES Run Options
Traditional LES (idealized)
  horizontal grid spacing (∆) from 20 m to 80 m
Nudged LES (realistic CBL)
  OU-LES (∆ = 40 m) is nudged with
  RUC output
  WRF model output

## Slide 8: Object of Study
Stull (1988) defines the CBL as a mixed layer dominated by buoyant turbulence generation
LES approach has proven to be particularly relevant for the reproduction of daytime CBL flow types
Find optimal method to obtain near-surface turbulent fluctuations and parameters which are important for EM and acoustic wave propagation

## Slide 9: Mesoscale Modeling: Background
Scales of motion associated with atmospheric turbulence are not resolved
Combined effects of subgrid turbulence must be modeled
Horizontal turbulent exchange → Smagorinsky-type closure
Vertical turbulent exchange → parameterized via turbulence (PBL) scheme
Notes: Cheapest option
PBL schemes assume that an individual model grid cell contains a representative sample of subgrid turbulent motions
Smagorinsky is based on deformation of resolved flow

## Slide 10: Mesoscale Modeling: Setup
Expanded work from previous studies
  Gibbs (2008), Gibbs et al. (2011)
Five CBL cases investigated
Comparison domain centered over ARM site in Lamont, OK
WRF model output compared with observational and OU-LES data
Notes: Four PBL schemes tested: YSU, MYJ, MYNN, TEMF
  WRF: 101 x 101 x 41 (∆x = ∆y = 1 km), Initialized with NARR data (∆ ~ 32 km), 12-hr warm-start to reduce spin-up effects
  LES: 512 x 512 x 80 (∆x = ∆y = 100 m, ∆z = 50m), Nudged with RUC data (∆ ~ 20 km)
  OBS: SMOS, CO2FLX, ECOR

## Slide 11: Mesoscale Modeling: Setup

## Slide 12: Mesoscale Modeling: Discussion
Little value added for horizontal grid spacing refinement of 4 km → 1 km
These scales often reside within the maximum energy-containing spectral intervals of CBL motions
Notes: Energy-containing = turbulence producing
  Flow features are potentially neither sufficiently resolved explicitly nor correctly represented statistically as subgrid-scale phenomena (Wyngaard 2004)

## Slide 13: Mesoscale Modeling: Discussion
WRF mean fields compared reasonably well with observational and LES data
Turbulence parameters indicated WRF generally failed to capture small-scale spatial variability of CBL flows
Non-local PBL scheme (YSU) performed the most admirably across a broad range of conditions
Notes:   Some issues with shallow PBL and cool bias
  Findings match other studies (Shin and Hong 2011)

## Slide 14: Large Eddy Simulation: Background
Historically, the LES approach has proven particularly relevant for the reproduction of CBL flow types
Equations of motion are filtered in physical space to remove smallest scales of the flow
Large scale eddies are explicitly resolved
Effects of small scales are modeled
Notes:   OU-LES uses implicit box filter (grid cutoff)
  Small scales more favorable to generalized modeling
  Given sufficient resolution, LES is assumed independent of SFS model

## Slide 15: Idealized LES: Setup
CBL flows were reproduced using OU-LES and WRF-LES
Numerical domain: 10.24 × 10.24 × 2 km3
Initialized with same idealized profiles
Forcings were set equal and held constant
Effects of flow types (with/without shear) and of varying grid spacing were investigated
Notes: Velocity spectra and other statistics compared

## Slide 16: Idealized LES: Setup
Why Spectra?
Lack of verification data at these scales
Does model produce expected energy statistics?
Does model produce features consistent with realistic atmospheric dynamics?
Further allows investigation of model numerics and assessment of effective resolution
Notes: Velocity spectra and other statistics compared

## Slide 17: Idealized LES: Setup
Notes:   Come from WRF model idealized cases
  Goal is to quickly spin-up a well-developed CBL

## Slide 18: Idealized LES: Code Descriptions
 | OU-LES | WRF-LES
Governing Equations | Incompressible, Boussinesq | Compressible, Non-hydrostatic
Finite Difference Scheme | 2nd-order centered | 5th-order upwind
Integration Scheme | 3rd-order Runge-Kutta | 3rd-order Runge-Kutta (time-split)
Subgrid Scheme | 1.5-order TKE | 
Lateral Boundary Conditions | Periodic | 
Notes: WRF model has several filters:
1.) 5th-order = 6th-order + Implicit diffusion term, Diffusion term proportional to the Courant number
2.) Time-averaging of vertically-implicit part of time-split equations slightly forward-centered
3.) Terms added to horizontal momentum equations that specifically damp 3D divergence (in terms of time derivative of pressure)
--- Modified pressure used in horizontal pressure-gradient terms
4.) Terms added to horizontal momentum equations that damp the vertically-integrated horizontal divergence

## Slide 19: w-component velocity (z/zi = 0.25)
Notes: Sample slice of final hour. Looks similar, right? Some signs of broader, less organized cellular convection for free, and slightly broader and elongated streaks in shear.

## Slide 20: u-component: 1D spectral density (z/zi = 0.25)
Notes: Free: both have narrower inertial sub-range and much sharper drop-off, more energy at larger scales
Shear: similar, but still drops off faster, transverse worse

## Slide 21: u-component: 2D spectral density (z/zi = 0.25)
Notes: Note: elongated in transverse direction due to theory ~4/3 t/l
Free: WRF more concentrated near larger scales, and fast drop-off
Shear: Not as concentrated near larger scales, but drop-off occurs at smaller scales.
Note, spectra shifted in k2 direction, due to variability across rolls, these are small scale anisotropic effects that WRF washes out

## Slide 22
Notes: For instance, air pollution applications, where dispersive role of small-scale motion may be very important, or wave propagation business, where structure-function parameter will not be right if small-scale motions are affected by numerical dissipation.

## Slide 23: w-component: 1D spectral density (z/zi = 0.25)
Notes: Free: both have narrower inertial sub-range and much sharper drop-off, more similar energy at larger scales
Shear: k1 direction almost matches exactly, in k2 direction get larger drop-off more energy at larger scales

## Slide 24: w-component: 2D spectral density (z/zi = 0.25)
Notes: Note: not elongated because k1,k2 are both transverse
Free: WRF less more concentrated near larger scales, and fast drop-off
Shear: Not as concentrated near larger scales, but drop-off occurs at smaller scales.
Note, spectra shifted in k2 direction, due to variability across rolls, these are small scale anisotropic effects that WRF washes out

## Slide 25: normalized velocity variance
Notes: Free: u: WRF larger v: WRF larger w: similar at level of interest
Shear: u: OU larger v: similar w: WRF maybe slightly more at level of interest

## Slide 26: normalized turbulence kinetic energy
Notes: Free: tke: WRF larger
Shear: tke: OU larger

## Slide 27: Discussion: Shear-Free
Visually, velocity patterns look similar

## Slide 28: Discussion: Shear-Free
WRF-LES produced larger velocity variances, larger TKE
Notes: For instance, air pollution applications, where dispersive role of small-scale motion may be very important, or wave propagation business, where structure-function parameter will not be right if small-scale motions are affected by numerical dissipation.

## Slide 29: Discussion: Shear-Free
Spectra show that energy attributed to larger scales in WRF-LES as compared to OU-LES
Notes: For instance, air pollution applications, where dispersive role of small-scale motion may be very important, or wave propagation business, where structure-function parameter will not be right if small-scale motions are affected by numerical dissipation.

## Slide 30: Discussion: Shear-Free
WRF-LES had slightly narrower inertial sub-range, less effective resolution, and sharper drop-off at high frequencies

## Slide 31: Discussion: Shear-Driven
Visually, velocity patterns look similar

## Slide 32: Discussion: Shear-Driven
WRF-LES produced smaller u-variance, TKE, & momentum flux - larger velocities

## Slide 33: Discussion: Shear-Driven
Spectra show that k1 spectra match more closely, but for k2, similar behavior as in shear-free case
Notes: For instance, air pollution applications, where dispersive role of small-scale motion may be very important, or wave propagation business, where structure-function parameter will not be right if small-scale motions are affected by numerical dissipation.

## Slide 34: Discussion: Shear-Driven
2D spectra indicate that shear-induced, anisotropic effects are smudged out at small scales in WRF-LES
Notes: For instance, air pollution applications, where dispersive role of small-scale motion may be very important, or wave propagation business, where structure-function parameter will not be right if small-scale motions are affected by numerical dissipation.

## Slide 35: Idealized LES: Discussion
LES can be an expensive
WRF-LES (512x512x80) ~ 1200 proc. & 45 hrs.
OU-LES (512x512x80) ~ 1 proc. & 8-10 days
Output files ≥ 1 TB
Notes: Energy-containing = turbulence producing
  Flow features are potentially neither sufficiently resolved explicitly nor correctly represented statistically as subgrid-scale phenomena (Wyngaard 2004)

## Slide 36: Idealized LES: Discussion
WRF-LES suffers from excessive numerical dissipation at small scales
Appears dependent on dominant flow type
May result from filters in the dynamics solver
Possibly affects larger scales
Notes: Energy-containing = turbulence producing
  Flow features are potentially neither sufficiently resolved explicitly nor correctly represented statistically as subgrid-scale phenomena (Wyngaard 2004)

## Slide 37: Real-Data LES: Problems
Lateral boundaries are assumed periodic
Domains are generally disconnected from large-scale forcings & local terrain properties
OU-LES, for example, uses lower-order advection schemes
Notes: 1.) Periodic LBC condition not met in atmosphere
  2.) Predictions are susceptible to drift from observations and often fail to reproduce sharp gradients observed in nature
  3.) dispersive errors

## Slide 38: Real-Data LES: Solutions
1.) WRF-LES nested in mesoscale WRF model
Specified lateral boundaries
Higher-order finite-difference scheme
2.) Nudged OU-LES
connects LES with realistic data from the larger-scale environment
retains local variability by only modifying background environment
Notes: WRF-LES is convenient, one-stop shop

## Slide 39: Nested WRF-LES: Setup
Simulation Type | PBL Scheme | Spacing (m) | Mesh Size | Time Step (s)
Mesoscale | YSU | 12,960 | 100x100x100 | 20
 |  | 4,320 | 100x100x100 | 5
 |  | 1,440 | 100x100x100 | 1
LES | WRF-LES | 480 | 100x100x100 | 4/5
 |  | 160 | 100x100x100 | 1/5
 |  | 40 | 201x201x100 | 1/20

## Slide 40: Nudged OU-LES: Setup
Nudging profiles are linearly interpolated in time to current time step
That profile is subtracted from the plane-averaged LES profiles
The difference is modified by a nudging factor
That factor allows for an adjustment between the convective and diurnal time scales
Nudging tendency is applied at next time step
Notes: Only modifies the background environment
Allows local variability to be retained

## Slide 41: Case 1: June 7, 2007

## Slide 42: Case 1: nudging profiles
Notes: Cheapest option

## Slide 43: Case 1: meteogram
Notes: Sample slice of final hour. Looks similar, right? Some signs of broader, less organized cellular convection for free, and slightly broader and elongated streaks in shear.

## Slide 44: Case 1: u-component velocity (z/zi = 0.25)
Notes: Sample slice of final hour. Looks similar, right? Some signs of broader, less organized cellular convection for free, and slightly broader and elongated streaks in shear.

## Slide 45: Case 1: u-component 1D spectral density (z/zi=0.25)
Notes: Sample slice of final hour. Looks similar, right? Some signs of broader, less organized cellular convection for free, and slightly broader and elongated streaks in shear.

## Slide 46: Case 1: u-component 2D spectral density (z/zi=0.25)
Notes: Sample slice of final hour. Looks similar, right? Some signs of broader, less organized cellular convection for free, and slightly broader and elongated streaks in shear.

## Slide 47: Case 2: October 26, 2008

## Slide 48: Case 2: nudging profiles
Notes: Cheapest option

## Slide 49: Case 2: meteogram
Notes: Sample slice of final hour. Looks similar, right? Some signs of broader, less organized cellular convection for free, and slightly broader and elongated streaks in shear.

## Slide 50: Case 2: u-component velocity (z/zi=0.25)
Notes: Sample slice of final hour. Looks similar, right? Some signs of broader, less organized cellular convection for free, and slightly broader and elongated streaks in shear.

## Slide 51: Case 2: u-component 1D spectral density (z/zi=0.25)
Notes: Sample slice of final hour. Looks similar, right? Some signs of broader, less organized cellular convection for free, and slightly broader and elongated streaks in shear.

## Slide 52: Case 2: u-component 2D spectral density (z/zi=0.25)
Notes: Sample slice of final hour. Looks similar, right? Some signs of broader, less organized cellular convection for free, and slightly broader and elongated streaks in shear.

## Slide 53: Nested WRF-LES: Discussion
Only two cases were shown due to instabilities in other cases
Split-nesting procedure is non-standard and potentially expensive
LES domains ~ 384 proc. & 40 hrs.
Notes:   Even with extremely conservative time step, WRF-LES domains would crash
  Possibly due to limits on time step and the initial transition into turbulent flow

## Slide 54: Nested WRF-LES: Discussion
Mean near-surface fields generally matched favorably with comparison data
Slices showed big streaks, no variability associated with atmospheric turbulence
Resulting high-order statistics were corrupted
WRF-LES fails to adequately reproduce spatial variability within sufficiently broad scale ranges
Notes:   Even with extremely conservative time step, WRF-LES domains would crash
  Possibly due to limits on time step and the initial transition into turbulent flow

## Slide 55: Nested WRF-LES: Discussion
Behavior possibly due to boundary effects
Matching SGS closures across nests is problematic
Coarser domains do not sufficiently resolve TKE
Model numerics may also pose problems
Required tradeoffs may limit the applicability of WRF-LES in particular real-data scenarios
Notes: described in previous studies (Moeng et al. 2007; Mirocha 2010)
Not enough TKE to pass to iner domains, must spin up
Outer LES domains likely reside within problematic scale ranges

## Slide 56: Nudged OU-LES: Discussion
How applicable this procedure is across scales and geographic locations remains a question for future study
Nudging procedure improves mean near-surface fields
Turbulence structures that OU-LES is known to confidently reproduce are retained
Notes:   that OU-LES is known to confidently reproduce

## Slide 57: Nudged OU-LES: Discussion
Overall, the higher-resolution WRF-nudged simulations best accomplish this task
Best compromise in reproducing accurate bulk meteorological quantities and realistic turbulence statistics across a broad range of scales.
Notes:   in space and time

## Slide 58: Summary
WRF-LES solves more physically robust equations, but filters affect scales of interest (and maybe others)
WRF-LES uses a higher-order advection scheme, but implicit diffusion term may also affect scales of interest
Notes:   in space and time

## Slide 59: Summary
OU-LES uses periodic LBCs, which aren’t as physically relevant.
Specified boundaries and nesting in WRF-LES affect scales of interest
OU-LES may then be nudged, but the implementation is rather ad-hoc
Users must weight tradeoffs